## Slide 1
Emergent Room Acoustic Resonance Analysis via
Multi-Algorithm Feedback Detection
Don Wells
Kill The Ring Project • killthering.com • March 2026
KEY RESULT
‖S_fb − S_rm‖₂ → 0
Room resonances and feedback are
spectrally indistinguishable to all
six detection algorithms
ABSTRACT
We present the observation that a real-time acoustic feedback detection system, when operated at elevated sensitivity without an active electroacoustic feedback loop, produces EQ correction recommendations corresponding to room resonance modes. The system employs six fused detection algorithms — Magnitude Slope Deviation (MSD), phase coherence analysis, spectral flatness, comb filter pattern detection, inter-harmonic ratio (IHR), and peak-to-median ratio (PTMR) — augmented by a neural network meta-model. We demonstrate that room resonances produce spectral signatures physically indistinguishable from acoustic feedback to these algorithms, enabling real-time room analysis requiring no test signal, no calibration microphone, and no prior room configuration.
THE PROBLEM
Professional room analyzers (Smaart, REW, Dirac Live) require:
• Calibrated measurement microphone ($200+)
• Test signal generator (pink noise, swept sine)
• Empty venue (no audience)
• 15-30 minutes setup time
• Specialized software ($400-$800+)
No existing tool can analyze room acoustics:
• In real-time during live performance
• With audience present
• Using ambient sound as excitation
• With zero setup or calibration
PHYSICAL EQUIVALENCE
ACOUSTIC FEEDBACK
• Sustained by electroacoustic loop
(mic → amp → speaker → air → mic)
• Persistent narrowband peak
• Stable magnitude (low MSD)
• High phase coherence
• High Q factor
ROOM RESONANCE
• Sustained by wall reflections
(standing wave in enclosure)
• Persistent narrowband peak
• Stable magnitude (low MSD)
• High phase coherence
• High Q factor
=
The only difference is the sustaining mechanism — invisible to spectral analysis.
Both satisfy identical spectral stability criteria for all six detection algorithms.
Room Mode Eigenfrequencies (Rayleigh):
f(nₓ,nᵧ,nz) = (c/2)√((nₓ/L)² + (nᵧ/W)² + (nz/H)²)
Schroeder frequency: f_S = 2000√(T₆₀/V)
SYSTEM ARCHITECTURE
MAIN THREAD
AudioContext → 8192-pt FFT
Peak detection (50fps)
Prominence + persistence
WEB WORKER
6 algorithms + ML model
Content-adaptive fusion
5 multiplicative gates
OUTPUT
EQ advisory generation
GEQ/PEQ/shelf recs
ERB psychoacoustic scaling
→
→
SIX DETECTION ALGORITHMS
MSD
Magnitude stability
Second-derivative stencil
Sparse pool: 256 slots
MSD(k)=(1/N)Σ|G''|²
Phase
Phase coherence
Circular statistics
phasor averaging
C=|mean(e^{jΔφ})|
Spectral
Spectral flatness
Geometric/arithmetic
mean ratio + kurtosis
SF=G_mean/A_mean
Comb
Comb filter
Harmonic series
matching ±5%
Δf = c/d
IHR*
Inter-harmonic ratio
Sideband energy
analysis (NOVEL)
E_inter/E_harmonic
PTMR*
Peak-to-median
Peak sharpness vs
neighborhood (NOVEL)
peak−median(±20)
* Novel algorithms (not found in prior literature)
CONTENT-ADAPTIVE WEIGHT PROFILES
Algorithm | DEFAULT | SPEECH | MUSIC | COMP
MSD | 0.27 | 0.30 | 0.07 | 0.11
Phase Coherence | 0.23 | 0.22 | 0.32 | 0.27
Spectral Flatness | 0.11 | 0.09 | 0.09 | 0.16
Comb Pattern | 0.07 | 0.04 | 0.07 | 0.07
IHR | 0.12 | 0.09 | 0.22 | 0.16
PTMR | 0.10 | 0.16 | 0.13 | 0.13
ML Meta-Model | 0.10 | 0.10 | 0.10 | 0.10
MULTIPLICATIVE GATES
Gate | Multiplier | Purpose | Room Mode?
IHR Gate | ×0.65 | Suppress instruments (harmonics > 3) | NOT TRIGGERED
PTMR Gate | ×0.80 | Suppress broad peaks | NOT TRIGGERED
Comb Stability | ×0.25 | Suppress sweeping effects | NOT TRIGGERED
Formant Gate | ×0.65 | Suppress sustained vowels | NOT TRIGGERED
Chromatic Gate | ×0.60 | Suppress Auto-Tune | NOT TRIGGERED
Room modes pass through the entire detection pipeline without suppression.
ALGORITHM SCORE COMPARISON
Room Resonance vs. Acoustic Feedback — All Six Algorithms
Algorithm | Room Mode | Feedback | Verdict
MSD | ≈ 0 (stable) | ≈ 0 (stable) | IDENTICAL
Phase Coherence | 0.85-0.95 | 0.85-0.95 | IDENTICAL
Spectral Flatness | < 0.05 (tonal) | < 0.05 (tonal) | IDENTICAL
Comb Pattern | Matches axial | Matches loop | IDENTICAL
IHR | ≈ 0 (clean) | ≈ 0 (pure tone) | IDENTICAL
PTMR | High (narrow) | High (narrow) | NEAR-IDENTICAL
COMPARISON WITH EXISTING TOOLS
Feature | KTR | Smaart | REW | Dirac
Test signal | None | Pink noise | Sweep | Sweep
Cal. mic | None | Required | Required | Required
Real-time | 50fps | Yes | No | No
Audience OK | Yes | Difficult | No | No
Setup time | 0 sec | 15-30m | 10-20m | 15-30m
EQ output | Auto | Manual | Manual | Auto
Cost | Free | $800+ | Free | $400+
SAMPLE EQ ADVISORY OUTPUT
FREQ NOTE Q CUT SEVERITY
127 Hz B2 12.4 -3.8 dB MODERATE
247 Hz B3 8.3 -4.2 dB MODERATE
312 Hz D#4 15.1 -5.1 dB HIGH
498 Hz B4 10.7 -3.5 dB MODERATE
623 Hz D#5 6.2 -2.9 dB LOW
These values constitute a room correction filter specification — identical to
what Smaart or REW would produce, but generated in real-time from ambient sound.
LIMITATIONS
• Lower SNR than dedicated measurement signals
• No phase response measurement (magnitude-only)
• Cannot distinguish room modes from HVAC/structural vibration
• Ambient excitation energy distribution is uncontrolled
• Requires elevated sensitivity setting (threshold ≤ 8 dB)
CONCLUSIONS
1. Room resonances and acoustic feedback produce identical spectral signatures across all six detection algorithms.
2. A feedback detection system operated at elevated sensitivity inherently performs room acoustic analysis.
3. This emergent behavior enables real-time room analysis requiring zero setup: no test signal, no calibration microphone, no prior room configuration.
4. The system generates parametric EQ recommendations that constitute room correction filter specifications.
5. This discovery transforms a single-purpose feedback detector into a dual-purpose acoustic intelligence tool.
FUTURE WORK
1. Formal validation against calibrated room measurements (Smaart/REW comparison study)
2. Dedicated "Room Analysis" mode with room resonance labeling and Schroeder frequency estimation
3. Cross-validation with impulse response measurements in controlled environments
4. Extended ML model training to distinguish room modes from feedback (optional classification)
5. Multi-microphone spatial analysis for room mode pattern identification
6. Integration with digital mixing consoles for automated room correction
SYSTEM PERFORMANCE
50 fps
Analysis frame rate
5.86 Hz
Frequency resolution (8192-pt FFT)
64 KB
MSD sparse pool memory
< 20 ms
Detection latency
929
ML model parameters
488
Automated test cases
REFERENCES
[1] Rohdenburg et al., "Magnitude Slope Deviation for Acoustic Feedback Detection," DAFx-16, 2016
[2] Hopkins, C., "Sound Insulation," Butterworth-Heinemann, 2007
[3] Glasberg & Moore, "Derivation of auditory filter shapes," Hearing Research, 1990
[4] Schroeder, M.R., "The 'Schroeder frequency' revisited," JASA, 1996
[5] van Waterschoot & Moonen, "Fifty Years of Acoustic Feedback Control," Proc. IEEE, 2011
[6] Rational Acoustics, "Smaart v8 User Guide," 2018
[7] Fisher, N.I., "Statistical Analysis of Circular Data," Cambridge, 1993
[8] Cooley & Tukey, "An Algorithm for Complex Fourier Series," Math. Comp., 1965
[9] Kuttruff, H., "Room Acoustics," 6th ed., CRC Press, 2016
[10] Wells, D., "Kill The Ring: Real-Time Acoustic Feedback Detection," 2026
Kill The Ring • killthering.com • Real-Time Acoustic Intelligence
US Provisional Patent Application Filed March 20, 2026 • AES Convention Paper Submitted • Open Source: github.com/donwellsav/killthering
Don Wells • don@killthering.com