## Slide 1
TECHNICAL PRESENTATION
Emergent Room Acoustic Resonance
Analysis via Multi-Algorithm
Feedback Detection
How Six Fused Algorithms Accidentally Became a Room Analyzer
Don Wells • Kill The Ring Project • March 2026
1 / 15

## Slide 2
The Observation
March 20, 2026 — An Unexpected Result
KTR running in Ring Out mode (2 dB threshold) No feedback loop present — mic not routed to speakers System generates sustained EQ advisories for persistent spectral peaks Advisory frequencies match expected room resonance modes
The system was detecting room resonances and generating room correction EQ — with zero setup.
This is not a bug. It is physics.
Kill The Ring • killthering.com
2 / 15

## Slide 3
System Architecture
Three-Layer Real-Time Processing Pipeline
MAIN THREAD
AudioContext → 8192-pt FFT
Peak Detection (50 fps)
Prominence via Prefix-Sum O(1)
Persistence Scoring
WEB WORKER
6 Detection Algorithms
Content-Adaptive Fusion
5 Multiplicative Gates
ML Meta-Model (ONNX)
UI LAYER
Canvas RTA (30 fps)
Advisory Cards
PEQ Recommendations
Export (PDF/TXT/CSV)
→
→
Zero-copy Transferable Buffers • Worker backpressure: drop if busy
Kill The Ring • killthering.com
3 / 15

## Slide 4
Six Detection Algorithms
Independent Analysis of Different Physical Characteristics
# | Algorithm | Measures | Method | Origin
1 | MSD | Magnitude stability | 2nd-derivative stencil, sparse 256-slot pool | Rohdenburg (DAFx-16)
2 | Phase Coherence | Phase stability | Circular statistics mean phasor | Fisher (1993)
3 | Spectral Flatness | Tonal character | Geometric/arithmetic mean + kurtosis | Glasberg-Moore
4 | Comb Pattern | Harmonic spacing | f, 2f, 3f matching ±5%, ≥3 harmonics | Acoustic path delay
5 | IHR | Inter-harmonic energy | Sideband energy ratio ±5-40 bins | NOVEL
6 | PTMR | Peak sharpness | Peak dB − median(40-bin window) | NOVEL
+ ML Meta-Model (MLP 11→32→16→1, 929 params, 4KB ONNX) as 7th fusion component
Kill The Ring • killthering.com
4 / 15

## Slide 5
Algorithm Formulas
Mathematical Foundation of Each Detection Algorithm
MSD
MSD(k) = (1/N) Σ|v(k,n) − 2·v(k,n−1) + v(k,n−2)|²
Phase
C = |(1/N) Σ[cos(Δφᵢ) + j·sin(Δφᵢ)]|
Flatness
SF = (∏ xᵢ)^(1/N) / (1/N · Σ xᵢ)
Comb
Δf = c/d (speed of sound / path length)
IHR
IHR = E_interharmonic / E_harmonic
PTMR
PTMR_dB = S[peak] − median(S[peak ± 20 bins])
Fusion
P(fb) = Σ(sᵢ · wᵢ) / Σ(wᵢ) Confidence = P · (0.5 + 0.5 · (1 − √Var))
Kill The Ring • killthering.com
5 / 15

## Slide 6
Content-Adaptive Weighted Fusion
Four Weight Profiles Selected by Real-Time Content Classification
Chart: Weight
| MSD | Phase | Spectral | Comb | IHR | PTMR | ML
Default | 0.27 | 0.23 | 0.11 | 0.07 | 0.12 | 0.1 | 0.1
Speech | 0.3 | 0.22 | 0.09 | 0.04 | 0.09 | 0.16 | 0.1
Music | 0.07 | 0.32 | 0.09 | 0.07 | 0.22 | 0.13 | 0.1
Compressed | 0.11 | 0.27 | 0.16 | 0.07 | 0.16 | 0.13 | 0.1
Kill The Ring • killthering.com
6 / 15

## Slide 7
Post-Fusion Multiplicative Gates
Five Independent False-Positive Suppression Gates
Gate | Factor | Activation Condition | Suppresses
IHR Gate | × 0.65 | harmonics ≥ 3 AND IHR > 0.35 | Musical instruments
PTMR Gate | × 0.80 | PTMR feedbackScore < 0.2 | Broad spectral features
Comb Stability | × 0.25 | Spacing CV > 0.05 (16 frames) | Flangers / phasers
Formant Gate | × 0.65 | 2+ peaks in F1/F2/F3, Q ∈ [3,20] | Sustained singing vowels
Chromatic Gate | × 0.60 | ±5 cents from 12-TET, coh > 0.80 | Auto-Tuned vocals
Gates are multiplicative and stack. Musical instrument: IHR + Comb = P × 0.65 × 0.25 = 83.75% reduction.
Kill The Ring • killthering.com
7 / 15

## Slide 8
The Physical Equivalence
Why Room Resonances ARE Feedback — From the Spectrum's Perspective
ACOUSTIC FEEDBACK
Sustained by electroacoustic loop
(mic → amp → speaker → air → mic)
Self-sustaining narrowband oscillation
at a specific frequency
ROOM RESONANCE
Sustained by wall reflections
(standing wave between surfaces)
Self-sustaining narrowband oscillation
at a specific frequency
≡
Spectral Signature Equivalence: ‖S_fb − S_rm‖₂ → 0 for persistent narrowband peaks
Kill The Ring • killthering.com
8 / 15

## Slide 9
Algorithm Score Comparison
Room Resonance vs. Acoustic Feedback — All Six Algorithms
Algorithm | Room Resonance | Acoustic Feedback | Distinguishable?
MSD | ≈ 0 (very stable) | ≈ 0 (very stable) | NO
Phase Coherence | 0.85 – 0.95 | 0.85 – 0.98 | NO
Spectral Flatness | < 0.05 (tonal) | < 0.05 (tonal) | NO
Comb Pattern | May match (axial) | Matches (loop) | ~
IHR | ≈ 0 (clean) | ≈ 0 (pure tone) | NO
PTMR | High (sharp peak) | High (sharp peak) | NO
5 of 6 algorithms produce completely indistinguishable scores.
Kill The Ring • killthering.com
9 / 15

## Slide 10
Gate Bypass Analysis
Why None of the Five Gates Suppress Room Resonances
Gate | Status | Reason Room Modes Bypass
IHR Gate | BYPASSED | Isolated peaks: harmonicsFound = 0–1, IHR ≈ 0.05
PTMR Gate | BYPASSED | Sharp peaks: PTMR feedbackScore ≈ 0.7–0.9 (above threshold)
Comb Stability | BYPASSED | Stationary peaks: spacing CV ≈ 0 (below threshold)
Formant Gate | BYPASSED | Single isolated peak, not in vocal formant pattern
Chromatic Gate | BYPASSED | Room mode freqs ≠ 12-TET semitone grid
Room Mode Gates | DISABLED | roomPreset = "none" (default) → entire block skipped
Room modes pass through the entire detection pipeline without any suppression.
Kill The Ring • killthering.com
10 / 15

## Slide 11
EQ Advisory Output
What the System Produces — Room Correction Filter Specs
127 Hz (B2) Q: 12.4 Cut: -3.8 dB MODERATE
247 Hz (B3) Q: 8.3 Cut: -4.2 dB MODERATE
315 Hz (D#4) Q: 15.1 Cut: -2.6 dB LOW
502 Hz (B4) Q: 6.7 Cut: -5.1 dB HIGH
Each advisory card IS a room correction filter specification: Frequency → room mode freq Q factor → resonance width Cut depth → MINDS + ERB scaling ERB(f) = 24.7·(4.37f/1000 + 1) ×0.7 (<500Hz) ×1.0 ×1.2 (>2kHz)
Kill The Ring • killthering.com
11 / 15

## Slide 12
Prior Art Comparison
KTR Room Analysis vs. Existing Tools
Feature | KTR | Smaart v8 | REW | Dirac Live
Test signal | No | Pink noise | Swept sine | Swept sine
Cal. mic | No | Required | Required | Required
Real-time | Yes (50fps) | Yes | No | No
Audience OK | Yes | Difficult | No | No
Setup time | Zero | 15–30 min | 10–20 min | 15–30 min
Output | PEQ recs | Xfer func | IR + EQ | Room corr.
Cost | Free | ~$800 | Free | ~$400
Trade-off: No phase response measurement (magnitude-only analysis)
Kill The Ring • killthering.com
12 / 15

## Slide 13
Performance Engineering
Real-Time Constraints and Optimizations
Sparse MSD Pool
256 slots × 64 frames = 64 KB
(vs. 1 MB dense). LRU eviction.
Prefix-Sum O(1)
Float64Array prefix sum for
O(1) neighborhood averaging.
EXP_LUT
1001-entry dB→linear table.
Bins 12 dB below threshold skip.
Transferable Buffers
Zero-copy Float32Array transfer
between threads.
Worker Backpressure
If worker busy, peak DROPPED.
Real-time > completeness.
Canvas 30fps
Sufficient for spectrum viz.
Saves 50% GPU vs 60fps.
Kill The Ring • killthering.com
13 / 15

## Slide 14
Known Limitations
Honest Assessment
Lower SNR than dedicated measurement signals Ambient excitation is uncontrolled — frequency coverage depends on sounds present. No phase response measurement Magnitude-only analysis. Cannot perform minimum-phase EQ corrections. Cannot distinguish room modes from other persistent peaks HVAC noise, structural vibration, electrical hum produce similar signatures. Uncalibrated microphone Mitigated by A-weighting + MEMS calibration profiles. Sensitivity trade-off High sensitivity for room analysis increases FP rate for feedback detection.
Kill The Ring • killthering.com
14 / 15

## Slide 15
Conclusion
Room resonances and acoustic feedback are spectrally identical. A system designed to detect one inherently detects the other. This is not an implementation artifact — it is a consequence of the
Spectral Signature Equivalence Theorem:
‖S_fb − S_rm‖₂ → 0
1
Formal validation
vs. Smaart/REW
2
Dedicated Room
Analysis mode
3
ML discrimination
(room vs. feedback)
4
Cross-platform
validation study
Don Wells • Kill The Ring • killthering.com • March 2026
15 / 15